/*****************************************************************/
/* "Micro42" SSB QRP TRX */
/* Display OLED SSD1306 64x32 */
/* ************************************************************ */
/* MUC: ATMEL AVR ATmega168, 8 MHz */
/* */
/* Compiler: GCC (GNU AVR C-Compiler) */
/* Author: Peter Rachow (DK7IH) */
/* Last change: OCT 2017 */
/*****************************************************************/

//PORTS
//OUTPUT
//PB0..PB2: DDS

//INPUT
//PC0: =ADC0: Pull-up for key switches with various resistors against GND
//PC1: =ADC1: AGC voltage for S-Meter
//PC2: =ADC3: TX PWR meter
//PC3: =ADC3: Voltage measurement

//PD1: TX/RX indicator
//PD5, PD6: Rotary encoder

//TWI
//PC4=SDA, PC5=SCL: I²C-Bus lines:

#include <inttypes.h>
#include <stdio.h>
#include <stdlib.h>
#include <math.h>
#include <avr/interrupt.h>
#include <avr/io.h>
#include <avr/sleep.h>
#include <avr/eeprom.h>
#include <util/delay.h>
#include <util/twi.h>

#undef F_CPU
#define F_CPU 16000000
#define INTERFREQUENCY 9000000

////////////////
// SPI for DDS
////////////////
#define DDSPORT PORTB
#define FSNYC 1 //green PB0
#define SDATA 2 //white PB1
#define SCLK 4 //blue PB2

//////////////////////////////////////
// L C D
//////////////////////////////////////

// Font 5x8 for OLED
const char fontchar[485] = {
0x00,0x00,0x00,0x00,0x00, // 20 space ASCII table for NOKIA LCD: 96 rows * 5 bytes= 480 bytes
0x00,0x00,0x5f,0x00,0x00, // 21 ! Note that this is the same set of codes for character you
0x00,0x07,0x00,0x07,0x00, // 22 " would find on a HD44780 based character LCD.
0x14,0x7f,0x14,0x7f,0x14, // 23 # Also, given the size of the LCD (84 pixels by 48 pixels),
0x24,0x2a,0x7f,0x2a,0x12, // 24 $ the maximum number of characters per row is only 14.
0x23,0x13,0x08,0x64,0x62, // 25 %
0x36,0x49,0x55,0x22,0x50, // 26 &
0x00,0x05,0x03,0x00,0x00, // 27 '
0x00,0x1c,0x22,0x41,0x00, // 28 (
0x00,0x41,0x22,0x1c,0x00, // 29 )
0x14,0x08,0x3e,0x08,0x14, // 2a *
0x08,0x08,0x3e,0x08,0x08, // 2b +
0x00,0x50,0x30,0x00,0x00, // 2c ,
0x08,0x08,0x08,0x08,0x08, // 2d -
0x00,0x60,0x60,0x00,0x00, // 2e .
0x20,0x10,0x08,0x04,0x02, // 2f /
0x3e,0x51,0x49,0x45,0x3e, // 30 0
0x00,0x42,0x7f,0x40,0x00, // 31 1
0x42,0x61,0x51,0x49,0x46, // 32 2
0x21,0x41,0x45,0x4b,0x31, // 33 3
0x18,0x14,0x12,0x7f,0x10, // 34 4
0x27,0x45,0x45,0x45,0x39, // 35 5
0x3c,0x4a,0x49,0x49,0x30, // 36 6
0x01,0x71,0x09,0x05,0x03, // 37 7
0x36,0x49,0x49,0x49,0x36, // 38 8
0x06,0x49,0x49,0x29,0x1e, // 39 9
0x00,0x36,0x36,0x00,0x00, // 3a :
0x00,0x56,0x36,0x00,0x00, // 3b ;
0x08,0x14,0x22,0x41,0x00, // 3c <
0x14,0x14,0x14,0x14,0x14, // 3d =
0x00,0x41,0x22,0x14,0x08, // 3e >
0x02,0x01,0x51,0x09,0x06, // 3f ?
0x32,0x49,0x79,0x41,0x3e, // 40 @
0x7e,0x11,0x11,0x11,0x7e, // 41 A
0x7f,0x49,0x49,0x49,0x36, // 42 B
0x3e,0x41,0x41,0x41,0x22, // 43 C
0x7f,0x41,0x41,0x22,0x1c, // 44 D
0x7f,0x49,0x49,0x49,0x41, // 45 E
0x7f,0x09,0x09,0x09,0x01, // 46 F
0x3e,0x41,0x49,0x49,0x7a, // 47 G
0x7f,0x08,0x08,0x08,0x7f, // 48 H
0x00,0x41,0x7f,0x41,0x00, // 49 I
0x20,0x40,0x41,0x3f,0x01, // 4a J
0x7f,0x08,0x14,0x22,0x41, // 4b K
0x7f,0x40,0x40,0x40,0x40, // 4c L
0x7f,0x02,0x0c,0x02,0x7f, // 4d M
0x7f,0x04,0x08,0x10,0x7f, // 4e N
0x3e,0x41,0x41,0x41,0x3e, // 4f O
0x7f,0x09,0x09,0x09,0x06, // 50 P
0x3e,0x41,0x51,0x21,0x5e, // 51 Q
0x7f,0x09,0x19,0x29,0x46, // 52 R
0x46,0x49,0x49,0x49,0x31, // 53 S
0x01,0x01,0x7f,0x01,0x01, // 54 T
0x3f,0x40,0x40,0x40,0x3f, // 55 U
0x1f,0x20,0x40,0x20,0x1f, // 56 V
0x3f,0x40,0x38,0x40,0x3f, // 57 W
0x63,0x14,0x08,0x14,0x63, // 58 X
0x07,0x08,0x70,0x08,0x07, // 59 Y
0x61,0x51,0x49,0x45,0x43, // 5a Z
0x00,0x7f,0x41,0x41,0x00, // 5b [
0x02,0x04,0x08,0x10,0x20, // 5c Yen Currency Sign
0x00,0x41,0x41,0x7f,0x00, // 5d ]
0x04,0x02,0x01,0x02,0x04, // 5e ^
0x40,0x40,0x40,0x40,0x40, // 5f _
0x00,0x01,0x02,0x04,0x00, // 60 `
0x20,0x54,0x54,0x54,0x78, // 61 a
0x7f,0x48,0x44,0x44,0x38, // 62 b
0x38,0x44,0x44,0x44,0x20, // 63 c
0x38,0x44,0x44,0x48,0x7f, // 64 d
0x38,0x54,0x54,0x54,0x18, // 65 e
0x08,0x7e,0x09,0x01,0x02, // 66 f
0x0c,0x52,0x52,0x52,0x3e, // 67 g
0x7f,0x08,0x04,0x04,0x78, // 68 h
0x00,0x44,0x7d,0x40,0x00, // 69 i
0x20,0x40,0x44,0x3d,0x00, // 6a j
0x7f,0x10,0x28,0x44,0x00, // 6b k
0x00,0x41,0x7f,0x40,0x00, // 6c l
0x7c,0x04,0x18,0x04,0x78, // 6d m
0x7c,0x08,0x04,0x04,0x78, // 6e n
0x38,0x44,0x44,0x44,0x38, // 6f o
0x7c,0x14,0x14,0x14,0x08, // 70 p
0x08,0x14,0x14,0x18,0x7c, // 71 q
0x7c,0x08,0x04,0x04,0x08, // 72 r
0x48,0x54,0x54,0x54,0x20, // 73 s
0x04,0x3f,0x44,0x40,0x20, // 74 t
0x3c,0x40,0x40,0x20,0x7c, // 75 u
0x1c,0x20,0x40,0x20,0x1c, // 76 v
0x3c,0x40,0x30,0x40,0x3c, // 77 w
0x44,0x28,0x10,0x28,0x44, // 78 x
0x0c,0x50,0x50,0x50,0x3c, // 79 y
0x44,0x64,0x54,0x4c,0x44, // 7a z
0x00,0x08,0x36,0x41,0x00, // 7b <
0x00,0x00,0x7f,0x00,0x00, // 7c |
0x00,0x41,0x36,0x08,0x00, // 7d >
0x10,0x08,0x08,0x10,0x08, // 7e Right Arrow ->
0x78,0x46,0x41,0x46,0x78, // 7f Left Arrow <-
0x00,0x06,0x09,0x09,0x06}; // 80 °

///////////////////////////
// DECLARATIONS
///////////////////////////
//
//I²C
void TWIInit(void);
void TWIStart(void);
void TWIStop(void);
uint8_t TWIReadACK(void);
uint8_t TWIReadNACK(void);
uint8_t TWIGetStatus(void);

//OLED
void oled_command(int value);
void oled_init(void);
void oled_write_byte(int col, int page, int val);
void oled_cls(void);
void oled_putchar1(int, int, char, int);
void oled_putstring(int, int, char *, int);
void oled_putnumber(int, int, long, int, int);
void oled_clear_section(int, int, int);
int xp2(int xp);

//String
int int2asc(long num, int dec, char *buf, int buflen);
int strlen(char *s);

//Hi DISPLAY
void show_frequency(long);
void show_tstep(int, int);
void show_meter(int);
void show_txrx(int);
void show_voltage(int);

//ADC
int get_keys(void);
int get_adc(int);

//AD9835 SPI
void spi_send_word(unsigned int);
void set_frequency(long, int);

//EEPROM
long load_frequency(void);
void store_frequency(long);

//MISC
int main(void);

///////////////////////////
// GLOBAL VARS
///////////////////////////
char *oldbuf = " ";
int laststate = 0; //Last state of rotary encoder
int tuningknob = 0;

//Tuning steps available
#define MAXTSTEPS 6 //Highest index of tsteps = n-1
#define STDTSTEP 2 //Standard tuning step
int n_tstep[] = {10, 50, 100, 250, 500, 1000, 5000};
int cur_tstep = STDTSTEP;

//SIDEBAND
#define MAXMODES 2
int sideband = 0; //Current sideband in use USB=0, LSB=1
unsigned long f_bfo[] = {9001500, 8998500}; //LO FREQUENCIES 10.7MHz
//unsigned long f_bfo[] = {10697000, 10693000}; //LO FREQUENCIES 10.7MHz

//METER
int sv_old = 0;

///////////////////////////
//
// TWI
//
///////////////////////////
void twi_init(void)
{
    //set SCL to 400kHz
    TWSR = 0x00;
    TWBR = 0x0C;

    //enable TWI
    TWCR = (1<<TWEN);
}

//Send start signal
void twi_start(void)
{
    TWCR = (1<<TWINT)|(1<<TWSTA)|(1<<TWEN);
    while ((TWCR & (1<<TWINT)) == 0);
}

//send stop signal
void twi_stop(void)
{
    TWCR = (1<<TWINT)|(1<<TWSTO)|(1<<TWEN);
}

void twi_write(uint8_t u8data)
{
    TWDR = u8data;
    TWCR = (1<<TWINT)|(1<<TWEN);
    while ((TWCR & (1<<TWINT)) == 0);
}

uint8_t TWIGetStatus(void)
{
    uint8_t status;
    //mask status
    status = TWSR & 0xF8;
    return status;
}

////////////////////////////////
//
// OLED commands
//
///////////////////////////////
//Send comand to OLED
void oled_command(int value)
{
   twi_start();
   twi_write(0x78); //Device address
   twi_write(0x00);
   twi_write(value);
   twi_stop();
}

//Initialize OLED
void oled_init(void)
{
    oled_command(0xae);

    oled_command(0xa8); //Multiplex ratio
    oled_command(0x2F);

    oled_command(0xd3); //Set display offset
    oled_command(0x00);

    oled_command(0x40 + 0x00); //Set display start line

    oled_command(0xa1);

oled_command(0x20); //Adressing mode
    oled_command(0x00); //HOR

    oled_command(0xc0);
    oled_command(0xc8);

    oled_command(0xda);
    oled_command(0x12);

    oled_command(0x81);
    oled_command(0xfF);
    oled_command(0xa4); //Display ON with RAM content
    oled_command(0xa6); //Normal display (Invert display = A7)
    oled_command(0xd5);
    oled_command(0x80);
    oled_command(0x8d);
    oled_command(0x14);
//oled_command(0x40); //Set display start line
    oled_command(0xAF); //Display ON

}

//Print character in normal size
//Write 8 vertical bits to given col (0..127) and page (0..7)
void oled_write_byte(int col, int page, int val)
{
    int t1;

//Col and line adr for OLED 68x32
oled_command(0x21); //COL (+32)
oled_command(col + 32 );
oled_command(col + 32);

oled_command(0x22); //PAGE (+2)
oled_command(page + 2);
oled_command(page + 2);

    twi_start();
twi_write(0x78);
twi_write(0x40); //Data
    for(t1 = 0; t1 < 7; t1++)
    {
        twi_write(val);
    }
twi_stop();
}

//Clear screen
void oled_cls(void)
{

    int x, y;
for(x = 0; x < 128; x++)
{
   for(y = 0; y < 8; y++)
{
   oled_write_byte(x, y, 0);
}
    }

}

//Print one character in normal size to OLED
void oled_putchar1(int col, int row, char ch1, int inv)
{
    int p, t1;
    char ch2;
int c = col;

    p = (5 * ch1) - 160;
    for(t1 = 0; t1 < 5; t1++)
    {
   if(!inv)
{
       ch2 = fontchar[p + t1];
}
else
{
       ch2 = ~fontchar[p + t1];
}

        oled_write_byte(c++, row, ch2);
    }

if(!inv)
{
   oled_write_byte(c, row, 0x00);
}
else
{
   oled_write_byte(c, row, 0xFF);
}

}

//2^x
int xp2(int xp)
{
    int t1, r = 1;
    for(t1 = 0; t1 < xp; t1++)
    {
        r <<= 1;
    }
    return r;

}

//Print string in given size
//lsize=0 => normal height, lsize=1 => double height
void oled_putstring(int col, int row, char *s, int inv)
{
    int c = col;

while(*s)
{
   oled_putchar1(c, row, *s++, inv);
c += 6;
}
}

//Print an integer/long to OLED
void oled_putnumber(int col, int row, long num, int dec, int inv)
{
    char *s = malloc(16);
if(s != NULL)
{
   int2asc(num, dec, s, 16);
   oled_putstring(col, row, s, inv);
   free(s);
}
}

void oled_clear_section(int x1, int x2, int row)
{
    int t1;
for(t1 = x1; t1 < x2; t1++)
{
   oled_write_byte(t1, row, 0);
}

}

/////////////////////////////////
//
// STRING FUNCTIONS
//
////////////////////////////////
//INT 2 ASC
int int2asc(long num, int dec, char *buf, int buflen)
{
    int i, c, xp = 0, neg = 0;
    long n, dd = 1E09;

    if(!num)
{
   *buf++ = '0';
*buf = 0;
return 1;
}

    if(num < 0)
    {
     neg = 1;
   n = num * -1;
    }
    else
    {
   n = num;
    }

    //Fill buffer with \0
    for(i = 0; i < 12; i++)
    {
   *(buf + i) = 0;
    }

    c = 9; //Max. number of displayable digits
    while(dd)
    {
   i = n / dd;
   n = n - i * dd;

   *(buf + 9 - c + xp) = i + 48;
   dd /= 10;
   if(c == dec && dec)
   {
       *(buf + 9 - c + ++xp) = '.';
   }
   c--;
    }

    //Search for 1st char different from '0'
    i = 0;
    while(*(buf + i) == 48)
    {
   *(buf + i++) = 32;
    }

    //Add minus-sign if neccessary
    if(neg)
    {
   *(buf + --i) = '-';
    }

    //Eleminate leading spaces
    c = 0;
    while(*(buf + i))
    {
   *(buf + c++) = *(buf + i++);
    }
    *(buf + c) = 0;

return c;
}

//STRLEN
int strlen(char *s)
{
   int t1 = 0;

   while(*(s + t1++));

   return (t1 - 1);
}

/////////////////////////////////
//
// DISPLAY FUNCTIONS
//
////////////////////////////////
//Current frequency (double letter height)
void show_frequency(long f)
{
char *buf;
int t1 = 0;

buf = malloc(10);

//Init buffer string
for(t1 = 0; t1 < 10; t1++)
{
   *(buf + t1) = 0;
}

int2asc(f / 10, 2, buf, 9);

//Display buffer (but only the letters that have changed)
for(t1 = 0; *(buf + t1); t1++)
{
if(*(oldbuf + t1) != *(buf + t1))
{
   oled_putchar1(10 + t1 * 6, 2, *(buf + t1), 0);
}
}

//Copy current buffer to storing variable
t1 = 0;
while(*(buf + t1))
{
*(oldbuf + t1) = *(buf + t1);
t1++;
}

free(buf);
}

//Current tuning step (Page 0)
void show_tstep(int n_step, int invert)
{
int xpos = 0, xlen = 5, ypos = 0;
    char *s_tstep[] = {"10Hz ", "50Hz ", "100Hz", "250Hz", "500Hz", "1kHz ", "5kHz "};

//Clear section of LCD
oled_clear_section(xpos * 6, xpos + xlen * 6, ypos );

//Write string to position
oled_putstring(0, ypos , s_tstep[n_step], invert);
}

//S-Meter bargraph (Page 6)
void show_meter(int sv0)
{
    int t1, sv;

sv = sv0;
if(sv == sv_old)
{
return;
}

    if(sv > 63)
{
   sv = 63;
}

//Clear bar graph partly, when new s-val smaller than previous
    if(sv < sv_old)
    {
    //Clear s-meter
    for(t1 = sv; t1 < 64; t1 += 3)
    {
        oled_write_byte(t1, 3, 0);
    }
        sv_old = sv;
        return;
    }

    //Draw bar graph
for(t1 = 0; t1 < sv; t1 += 3)//
{
   oled_write_byte(t1, 3, 0x1E);
}

    sv_old = sv;
}

void show_txrx(int status)
{
int xpos = 8, ypos = 0;

//Write string to position
if(status)
{
   oled_putstring(xpos * 6, ypos, "TX", 1);
}
else
{
   oled_putstring(xpos * 6, ypos, "RX", 0);
}

}

void show_voltage(int v1)
{
    char *buffer;
int t1, p;
int xpos = 5, ypos = 1;

buffer= malloc(0x10);
//Init buffer string
for(t1 = 0; t1 < 0x10; t1++)
{
   *(buffer + t1) = 0;
}
    p = int2asc(v1, 1, buffer, 6) * 6;
    oled_putstring(xpos * 6, ypos, buffer, 0);
oled_putstring(p + xpos * 6, ypos, "V ", 0);
free(buffer);
}

//////////////////////
//
// A D C
//
/////////////////////
//Read ADC value
int get_adc(int adc_channel)
{

int adc_val = 0;

ADMUX = (1<<REFS0) + adc_channel; // Kanal adcmode aktivieren
    _delay_ms(3);

    ADCSRA |= (1<<ADSC);
    //while(ADCSRA & (1<<ADSC));
_delay_ms(3);

adc_val = ADCL;
    adc_val += ADCH * 256;

return adc_val;

}

//Read keys via ADC0
int get_keys(void)
{

    int key_value[] = {97}; //PCB
    int t1;
    int adcval = get_adc(0);

    //TEST display of ADC value
    //oled_putstring(0, 3, "----", 0);
    //oled_putnumber(0, 3, adcval, -1, 0);

    if(adcval < 110 && adcval > 106) //Both buttons pressed simultanously PCB
    {
return 99;
}

    for(t1 = 0; t1 < 1; t1++)
    {
        if(adcval > key_value[t1] - 10 && adcval < key_value[t1] + 10)
        {
        return t1 + 1;
        }
    }
    return 0;
}

////////////////////////////////////////////////////
// INTERRUPT HANDLERS
////////////////////////////////////////////////////
//Rotary encoder
ISR(PCINT2_vect)
{

    int gray = (PIND & 0x60) >> 5; // Read PD5 and PD6

    int state = (gray >> 1) ^ gray; // Convert from Gray code to binary

    if (state != laststate) //Compare states
    {
        tuningknob += ((laststate - state) & 3) - 2; // Results in -1 or +1
        laststate = state;
    }
PCIFR |= (1 << PCIF0); // Clear pin change interrupt flag.
}

//************
// SPI
//************
void spi_send_word(unsigned int sbyte)
{
    unsigned int t1, x = 32768;
    for(t1 = 0; t1 < 16; t1++)
    {
        if(sbyte & x)
        {
        DDSPORT |= SDATA; //SDATA Bit PB1 set
        }
        else
        {
        DDSPORT &= ~(SDATA); //SDATA Bit PB1 erase
        }

        DDSPORT |= SCLK; //SCLK hi
        DDSPORT &= ~(SCLK); //SCLK lo

        x = x >> 1;
    }
    DDSPORT |= SDATA; //PB1 SDATA hi
}

void set_frequency(long f, int initddschip)
{
    long fxtal = 40000000; //fCrystal in Hz
    double fword0;
    long fword1;
    int t1;

    unsigned char xbyte[] = {0x33, 0x22, 0x31, 0x20};
    fword0 = (double) (INTERFREQUENCY - f) / fxtal;
    fword1 = (long) (fword0 * 0xFFFFFFFF);

    if(initddschip)
    {
        //init, set AD9835 to sleepmode
        DDSPORT &= ~(FSNYC); //FSYNC lo
        spi_send_word(0xF800);
        DDSPORT |= FSNYC; // FSYNC hi
    }

    //Send 4 * 16 Bit to DDS
    for(t1 = 0; t1 < 4; t1++)
    {
        DDSPORT &= ~(FSNYC); //FSYNC lo => Bit PB0 = 0
        spi_send_word((xbyte[t1] << 8) + (((fword1 >> ((3 - t1) << 3))) & 0xFF));
        DDSPORT |= FSNYC; // FSYNC hi => Bit PB0 = 1
    }

    //End of sequence
    DDSPORT &= ~(FSNYC); //FSYNC lo => Bit PB0 = 0
    if(initddschip)
    {
        //AD9835 wake up from sleep
        spi_send_word(0xC000);
    }
    else
    {
        //AD9835 freq data update, no full init
        spi_send_word(0x8000);
    }
    DDSPORT &= ~(FSNYC); //FSYNC lo => Bit PB0 = 0
}

//////////////////////
//
// E E P R O M
//
//////////////////////
void store_frequency(long f)
{
    long hiword, loword;
    unsigned char hmsb, lmsb, hlsb, llsb;

    int start_adr = 0;

cli();
    hiword = f >> 16;
    loword = f - (hiword << 16);
    hmsb = hiword >> 8;
    hlsb = hiword - (hmsb << 8);
    lmsb = loword >> 8;
    llsb = loword - (lmsb << 8);

    while(!eeprom_is_ready());
    eeprom_write_byte((uint8_t*)start_adr, hmsb);

    while(!eeprom_is_ready());
    eeprom_write_byte((uint8_t*)start_adr + 1, hlsb);

    while(!eeprom_is_ready());
    eeprom_write_byte((uint8_t*)start_adr + 2, lmsb);

    while(!eeprom_is_ready());
    eeprom_write_byte((uint8_t*)start_adr + 3, llsb);

    sei();

}

long load_frequency(void)
{
    long rf;
    unsigned char hmsb, lmsb, hlsb, llsb;
    int start_adr = 0;

    cli();
    hmsb = eeprom_read_byte((uint8_t*)start_adr);
    hlsb = eeprom_read_byte((uint8_t*)start_adr + 1);
    lmsb = eeprom_read_byte((uint8_t*)start_adr + 2);
    llsb = eeprom_read_byte((uint8_t*)start_adr + 3);
sei();

    rf = (long) 16777216 * hmsb + (long) 65536 * hlsb + (unsigned int) 256 * lmsb + llsb;

return rf;

}

int main(void)
{

    //OUTPUT
    DDRB = 0x07; //SPI for DDS AD9835

//INPUT
    PORTC = 0x31;//PC0: Pullup for key switches with various resistors against GND
        //I²C-Bus lines: PC4=SDA, PC5=SCL
    PORTD = 0x60;//Pullup resistors for PD5 and PD6 rotary encoder

//Operating frequencies
    long freq1;
    sideband = 1;

    //Keys, Tuning
int key = 0;
int loopcnt0 = 0;
int loopcnt2 = 0;

//TX-RX Indicator
int txrx = 0;

//Volts measurement
    int adc_v;
    double v1;
    int loopcnt1 = 16383;

    //Interrupt definitions for rotary encoder
PCMSK2 |= ((1<<PCINT21) | (1<<PCINT22)); //enable encoder pins as interrupt source
PCICR |= (1<<PCIE2); // enable pin change interupts

//ADC config and ADC init
    ADCSRA = (1<<ADPS0) | (1<<ADPS1) | (1<<ADEN); //Prescaler 64 and ADC on
get_adc(0); //One dummy conversion

    _delay_ms(100);
//TWI
twi_init();
_delay_ms(100);
//OLED
oled_init();
oled_cls();
    _delay_ms(100);

    freq1 = load_frequency();
    if(freq1 < 6995000 || freq1 > 7205000)
    {
freq1 = 7105000;
}

    set_frequency(freq1, 1);
    set_frequency(freq1, 1);
    show_frequency(freq1);
    show_tstep(cur_tstep, 0);
    show_txrx(0);

    sei();

    for(;;)
    {
/* //TEST
* for(freq1 = 7000000; freq1 < 7200000; freq1++)
{
set_frequency(freq1, 1);
}
*/

//Check if key pressed and meter
        if(loopcnt0++ > 16)
        {
   key = get_keys();
   loopcnt0 = 0;
}

if(!(PIND & 0x02)) //RX, cause PIND1 is 0
{
show_txrx(0);
if(txrx)
{
txrx = 0;
show_txrx(txrx);
set_frequency(freq1, 1);
}
}

if(PIND & 0x02) //TX, cause PIND1 is 1
{
show_txrx(1);
if(!txrx)
   {
txrx = 1;
show_txrx(txrx);
set_frequency(freq1, 1);
   }
}

if(txrx)
{
   show_meter(get_adc(2) >> 2); //TX
}
else
{
   show_meter(get_adc(1)); //RX
}

        key = get_keys();
if(key == 1)
{
while(get_keys());
if(cur_tstep < MAXTSTEPS)
{
cur_tstep++;
}
else
{
cur_tstep = 0;
}
show_tstep(cur_tstep, 0);
loopcnt2 = 0;
}

if(loopcnt1++ > 512)
{
        //CHECK VOLTAGE
   v1 = (double) get_adc(3) * 5 / 1024 * 4 * 10;
   adc_v = (int) v1;
      show_voltage(adc_v);
       loopcnt1 = 0;
   }

if(loopcnt2++ > 100 && cur_tstep != STDTSTEP)
{
//RESET TUNING STEP
cur_tstep = STDTSTEP;
show_tstep(cur_tstep, 0);
loopcnt2 = 0;
store_frequency(freq1);
        }

        //TUNING
        if(tuningknob > 2)
{
   freq1 -= n_tstep[cur_tstep];
   tuningknob = 0;
   set_frequency(freq1, 0);
show_frequency(freq1);
loopcnt2 = 0;
}

if(tuningknob < -2)
{
freq1 += n_tstep[cur_tstep];
   tuningknob = 0;
   set_frequency(freq1, 0);
show_frequency(freq1);
loopcnt2 = 0;
}

    }
return 0;
}