///////////////////////////////////////////////////////////////////
// ILI8341 Color LCD DEMO with ATMega644p //
// 8 bit parallel mode, 4 CTRLlines //
///////////////////////////////////////////////////////////////////
// Mikrocontroller: ATMEL AVR ATmega644p, 16 MHz //
// //
// Compiler: GCC (GNU AVR C-Compiler) //
// Author: Peter Baier (DK7IH) //
// OCT-2019 //
///////////////////////////////////////////////////////////////////
#define F_CPU 16000000

#include <inttypes.h>
#include <stdio.h>
#include <stdlib.h>
#include <math.h>
#include <avr/io.h>
#include <avr/interrupt.h>
#include <avr/sleep.h>
#include <avr/eeprom.h>
#include <util/delay.h>

//LCD ILI9341
//PAR line defines
#define LCDDATAPORT PORTD
#define LCDDATADDR DDRD
#define LCDCTRLPORT PORTB
#define LCDCTRLDDR DDRB
#define LCDRS 1 //CMD (low) or DATA (high)
#define LCDWR 2 //Write operation indicator (actice low)
#define LCDRD 4 //Read indicator (actice low)
#define LCDRES 8 //Reset (active low)

#define LCD_CMD 0
#define LCD_DATA 1

#define LCD_WIDTH 320
#define LCD_HEIGHT 240

#define WHITE 0xFFFF
#define SILVER1 0xC618
#define SILVER2 0xA510
#define BLACK 0x0000
#define GRAY 0x8410
#define LIGHT_GRAY 0xC618
#define LIGHT_GREEN 0x07E0
#define LIGHT_RED 0xF800
#define LIGHT_BLUE 0x03FF
#define RED 0xF800
#define MAROON1 0x8000
#define MAROON2 0x7800
#define FUCHSIA 0xF81F
#define PURPLE1 0x8010
#define PURPLE2 0x780F
#define LIME 0x07E0
#define GREEN 0x0400
#define YELLOW 0xFFE0
#define OLIVE1 0x8400
#define OLIVE2 0x7BE0
#define BLUE 0x001F
#define NAVY1 0x0010
#define NAVY2 0x000F
#define AQUA 0x07FF
#define TEAL 0x0410
#define DARK_BLUE 0x0002
#define MAGENTA 0xF81F
#define CYAN 0x07FF
#define DARK_CYAN 0x03EF
#define ORANGE 0xFCA0
#define BROWN 0x8200
#define VIOLET 0x9199
#define PINK 0xF97F
#define GOLD 0xA508

#define ROW1 220
#define ROW2 200
#define ROW3 180
#define ROW4 160
#define ROW5 140
#define ROW6 120
#define ROW7 100
#define ROW8 80
#define ROW9 60
#define ROW10 40
#define ROW11 20

//Font
#define FONTWIDTH 12
#define FONTHEIGHT 16
//Font 12x16 vert. MSB
const char xchar[][24]={
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x00
{0x00,0x00,0x03,0xF0,0x0C,0x0C,0x10,0x02,0x11,0x32,0x22,0x31,0x22,0x01,0x22,0x31,0x11,0x32,0x10,0x02,0x0C,0x0C,0x03,0xF0},	// 0x01
{0x00,0x00,0x03,0xF0,0x0F,0xFC,0x1F,0xFE,0x1E,0xCE,0x3D,0xCF,0x3D,0xFF,0x3D,0xCF,0x1E,0xCE,0x1F,0xFE,0x0F,0xFC,0x03,0xF0},	// 0x02
{0x00,0x00,0x00,0x00,0x00,0xF0,0x01,0xF8,0x03,0xF8,0x07,0xF0,0x0F,0xE0,0x07,0xF0,0x03,0xF8,0x01,0xF8,0x00,0xF0,0x00,0x00},	// 0x03
{0x00,0x00,0x00,0x00,0x00,0x80,0x01,0xC0,0x03,0xE0,0x07,0xF0,0x0F,0xF8,0x07,0xF0,0x03,0xE0,0x01,0xC0,0x00,0x80,0x00,0x00},	// 0x04
{0x00,0x00,0x03,0x80,0x07,0xC0,0x07,0xC0,0x13,0xB8,0x1B,0xFC,0x1F,0xFC,0x1B,0xFC,0x13,0xB8,0x07,0xC0,0x07,0xC0,0x03,0x80},	// 0x05
{0x00,0x00,0x00,0x00,0x03,0x80,0x07,0xC0,0x17,0xE0,0x1B,0xF0,0x1F,0xFC,0x1B,0xF0,0x17,0xE0,0x07,0xC0,0x03,0x80,0x00,0x00},	// 0x06
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x07
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x08
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x09
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x0A
{0x00,0x00,0x03,0x80,0x07,0xC0,0x0C,0x60,0x08,0x20,0x08,0x20,0x0C,0x60,0x07,0xC8,0x03,0xA8,0x00,0x18,0x00,0x78,0x00,0x00},	// 0x0B
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x70,0x08,0xF8,0x09,0x8C,0x3F,0x04,0x3F,0x04,0x09,0x8C,0x08,0xF8,0x00,0x70,0x00,0x00},	// 0x0C
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x0D
{0x00,0x00,0x06,0x00,0x0F,0x00,0x0F,0x00,0x07,0xFF,0x00,0x33,0x30,0x66,0x78,0xCC,0x79,0x98,0x3F,0xF0,0x00,0x00,0x00,0x00},	// 0x0E
{0x00,0x00,0x00,0x80,0x09,0xC8,0x07,0xF0,0x06,0x30,0x0C,0x18,0x3C,0x1E,0x0C,0x18,0x06,0x30,0x07,0xF0,0x09,0xC8,0x00,0x80},	// 0x0F
{0x00,0x00,0x00,0x00,0x00,0x00,0x1F,0xFC,0x0F,0xF8,0x07,0xF0,0x03,0xE0,0x01,0xC0,0x00,0x80,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x10
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x80,0x01,0xC0,0x03,0xE0,0x07,0xF0,0x0F,0xF8,0x1F,0xFC,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x11
{0x00,0x00,0x00,0x00,0x00,0x00,0x04,0x10,0x0C,0x18,0x1C,0x1C,0x3F,0xFE,0x1C,0x1C,0x0C,0x18,0x04,0x10,0x00,0x00,0x00,0x00},	// 0x12
{0x00,0x00,0x00,0x00,0x00,0x00,0x37,0xFE,0x37,0xFE,0x00,0x00,0x00,0x00,0x37,0xFE,0x37,0xFE,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x13
{0x00,0x00,0x00,0x38,0x00,0x7C,0x00,0xC6,0x00,0x82,0x3F,0xFE,0x3F,0xFE,0x00,0x02,0x3F,0xFE,0x3F,0xFE,0x00,0x02,0x00,0x00},	// 0x14
{0x00,0x00,0x00,0x00,0x08,0xDC,0x19,0xFE,0x11,0x22,0x11,0x22,0x11,0x22,0x11,0x22,0x1F,0xE6,0x0E,0xC4,0x00,0x00,0x00,0x00},	// 0x15
{0x00,0x00,0x00,0x00,0x00,0x00,0x38,0x00,0x38,0x00,0x38,0x00,0x38,0x00,0x38,0x00,0x38,0x00,0x38,0x00,0x38,0x00,0x00,0x00},	// 0x16
{0x00,0x00,0x00,0x00,0x00,0x00,0x44,0x08,0x4C,0x0C,0x5C,0x0E,0x7F,0xFF,0x5C,0x0E,0x4C,0x0C,0x44,0x08,0x00,0x00,0x00,0x00},	// 0x17
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x10,0x00,0x18,0x00,0x1C,0x3F,0xFE,0x00,0x1C,0x00,0x18,0x00,0x10,0x00,0x00,0x00,0x00},	// 0x18
{0x00,0x00,0x00,0x00,0x00,0x00,0x04,0x00,0x0C,0x00,0x1C,0x00,0x3F,0xFE,0x1C,0x00,0x0C,0x00,0x04,0x00,0x00,0x00,0x00,0x00},	// 0x19
{0x00,0x00,0x00,0x00,0x00,0x80,0x00,0x80,0x00,0x80,0x00,0x80,0x00,0x80,0x07,0xF0,0x03,0xE0,0x01,0xC0,0x00,0x80,0x00,0x00},	// 0x1A
{0x00,0x00,0x00,0x00,0x00,0x80,0x01,0xC0,0x03,0xE0,0x07,0xF0,0x00,0x80,0x00,0x80,0x00,0x80,0x00,0x80,0x00,0x80,0x00,0x00},	// 0x1B
{0x00,0x00,0x3F,0x00,0x20,0x00,0x20,0x00,0x20,0x00,0x20,0x00,0x20,0x00,0x20,0x00,0x20,0x00,0x20,0x00,0x20,0x00,0x00,0x00},	// 0x1C
{0x00,0x00,0x00,0x80,0x01,0xC0,0x03,0xE0,0x07,0xF0,0x00,0x80,0x00,0x80,0x00,0x80,0x07,0xF0,0x03,0xE0,0x01,0xC0,0x00,0x80},	// 0x1D
{0x00,0x00,0x04,0x00,0x06,0x00,0x07,0x00,0x07,0x80,0x07,0xC0,0x07,0xE0,0x07,0xC0,0x07,0x80,0x07,0x00,0x06,0x00,0x04,0x00},	// 0x1E
{0x00,0x00,0x00,0x20,0x00,0x60,0x00,0xE0,0x01,0xE0,0x03,0xE0,0x07,0xE0,0x03,0xE0,0x01,0xE0,0x00,0xE0,0x00,0x60,0x00,0x20},	// 0x1F
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x20
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x7C,0x33,0xFF,0x33,0xFF,0x00,0x7C,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x21
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x3C,0x00,0x3C,0x00,0x00,0x00,0x00,0x00,0x3C,0x00,0x3C,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x22
{0x00,0x00,0x02,0x00,0x1E,0x10,0x1F,0x90,0x03,0xF0,0x02,0x7E,0x1E,0x1E,0x1F,0x90,0x03,0xF0,0x02,0x7E,0x00,0x1E,0x00,0x10},	// 0x23
{0x00,0x00,0x00,0x00,0x04,0x78,0x0C,0xFC,0x0C,0xCC,0x3F,0xFF,0x3F,0xFF,0x0C,0xCC,0x0F,0xCC,0x07,0x88,0x00,0x00,0x00,0x00},	// 0x24
{0x00,0x00,0x30,0x00,0x38,0x38,0x1C,0x38,0x0E,0x38,0x07,0x00,0x03,0x80,0x01,0xC0,0x38,0xE0,0x38,0x70,0x38,0x38,0x00,0x1C},	// 0x25
{0x00,0x00,0x00,0x00,0x1F,0x00,0x3F,0xB8,0x31,0xFC,0x21,0xC6,0x37,0xE2,0x1E,0x3E,0x1C,0x1C,0x36,0x00,0x22,0x00,0x00,0x00},	// 0x26
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x27,0x00,0x3F,0x00,0x1F,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x27
{0x00,0x00,0x00,0x00,0x00,0x00,0x03,0xF0,0x0F,0xFC,0x1F,0xFE,0x38,0x07,0x20,0x01,0x20,0x01,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x28
{0x00,0x00,0x00,0x00,0x00,0x00,0x20,0x01,0x20,0x01,0x38,0x07,0x1F,0xFE,0x0F,0xFC,0x03,0xF0,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x29
{0x00,0x00,0x00,0x00,0x0C,0x98,0x0E,0xB8,0x03,0xE0,0x0F,0xF8,0x0F,0xF8,0x03,0xE0,0x0E,0xB8,0x0C,0x98,0x00,0x00,0x00,0x00},	// 0x2A
{0x00,0x00,0x00,0x00,0x01,0x80,0x01,0x80,0x01,0x80,0x0F,0xF0,0x0F,0xF0,0x01,0x80,0x01,0x80,0x01,0x80,0x00,0x00,0x00,0x00},	// 0x2B
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0xB8,0x00,0xF8,0x00,0x78,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x2C
{0x00,0x00,0x00,0x00,0x01,0x80,0x01,0x80,0x01,0x80,0x01,0x80,0x01,0x80,0x01,0x80,0x01,0x80,0x01,0x80,0x00,0x00,0x00,0x00},	// 0x2D
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x38,0x00,0x38,0x00,0x38,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x2E
{0x00,0x00,0x18,0x00,0x1C,0x00,0x0E,0x00,0x07,0x00,0x03,0x80,0x01,0xC0,0x00,0xE0,0x00,0x70,0x00,0x38,0x00,0x1C,0x00,0x0E},	// 0x2F
{0x00,0x00,0x07,0xF8,0x1F,0xFE,0x1E,0x06,0x33,0x03,0x31,0x83,0x30,0xC3,0x30,0x63,0x30,0x33,0x18,0x1E,0x1F,0xFE,0x07,0xF8},	// 0x30
{0x00,0x00,0x00,0x00,0x00,0x00,0x30,0x0C,0x30,0x0C,0x30,0x0E,0x3F,0xFF,0x3F,0xFF,0x30,0x00,0x30,0x00,0x30,0x00,0x00,0x00},	// 0x31
{0x00,0x00,0x30,0x1C,0x38,0x1E,0x3C,0x07,0x3E,0x03,0x37,0x03,0x33,0x83,0x31,0xC3,0x30,0xE3,0x30,0x77,0x30,0x3E,0x30,0x1C},	// 0x32
{0x00,0x00,0x0C,0x0C,0x1C,0x0E,0x38,0x07,0x30,0xC3,0x30,0xC3,0x30,0xC3,0x30,0xC3,0x30,0xC3,0x39,0xE7,0x1F,0x7E,0x0E,0x3C},	// 0x33
{0x00,0x00,0x03,0xC0,0x03,0xE0,0x03,0x70,0x03,0x38,0x03,0x1C,0x03,0x0E,0x03,0x07,0x3F,0xFF,0x3F,0xFF,0x03,0x00,0x03,0x00},	// 0x34
{0x00,0x00,0x0C,0x3F,0x1C,0x7F,0x38,0x63,0x30,0x63,0x30,0x63,0x30,0x63,0x30,0x63,0x30,0x63,0x38,0xE3,0x1F,0xC3,0x0F,0x83},	// 0x35
{0x00,0x00,0x0F,0xC0,0x1F,0xF0,0x39,0xF8,0x30,0xDC,0x30,0xCE,0x30,0xC7,0x30,0xC3,0x30,0xC3,0x39,0xC3,0x1F,0x80,0x0F,0x00},	// 0x36
{0x00,0x00,0x00,0x03,0x00,0x03,0x00,0x03,0x30,0x03,0x3C,0x03,0x0F,0x03,0x03,0xC3,0x00,0xF3,0x00,0x3F,0x00,0x0F,0x00,0x03},	// 0x37
{0x00,0x00,0x0F,0x00,0x1F,0xBC,0x39,0xFE,0x30,0xE7,0x30,0xC3,0x30,0xC3,0x30,0xC3,0x30,0xE7,0x39,0xFE,0x1F,0xBC,0x0F,0x00},	// 0x38
{0x00,0x00,0x00,0x3C,0x00,0x7E,0x30,0xE7,0x30,0xC3,0x30,0xC3,0x38,0xC3,0x1C,0xC3,0x0E,0xC3,0x07,0xE7,0x03,0xFE,0x00,0xFC},	// 0x39
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x1C,0x70,0x1C,0x70,0x1C,0x70,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x3A
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x9C,0x70,0xFC,0x70,0x7C,0x70,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x3B
{0x00,0x00,0x00,0x00,0x00,0xC0,0x01,0xE0,0x03,0xF0,0x07,0x38,0x0E,0x1C,0x1C,0x0E,0x38,0x07,0x30,0x03,0x00,0x00,0x00,0x00},	// 0x3C
{0x00,0x00,0x00,0x00,0x06,0x60,0x06,0x60,0x06,0x60,0x06,0x60,0x06,0x60,0x06,0x60,0x06,0x60,0x06,0x60,0x06,0x60,0x00,0x00},	// 0x3D
{0x00,0x00,0x00,0x00,0x30,0x03,0x38,0x07,0x1C,0x0E,0x0E,0x1C,0x07,0x38,0x03,0xF0,0x01,0xE0,0x00,0xC0,0x00,0x00,0x00,0x00},	// 0x3E
{0x00,0x00,0x00,0x1C,0x00,0x1E,0x00,0x07,0x00,0x03,0x37,0x83,0x37,0xC3,0x00,0xE3,0x00,0x77,0x00,0x3E,0x00,0x1C,0x00,0x00},	// 0x3F
{0x00,0x00,0x0F,0xF8,0x1F,0xFE,0x18,0x07,0x33,0xF3,0x37,0xFB,0x36,0x1B,0x37,0xFB,0x37,0xFB,0x36,0x07,0x03,0xFE,0x01,0xF8},	// 0x40
{0x00,0x00,0x38,0x00,0x3F,0x00,0x07,0xE0,0x06,0xFC,0x06,0x1F,0x06,0x1F,0x06,0xFC,0x07,0xE0,0x3F,0x00,0x38,0x00,0x00,0x00},	// 0x41
{0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x30,0xC3,0x30,0xC3,0x30,0xC3,0x30,0xC3,0x30,0xE7,0x39,0xFE,0x1F,0xBC,0x0F,0x00,0x00,0x00},	// 0x42
{0x00,0x00,0x03,0xF0,0x0F,0xFC,0x1C,0x0E,0x38,0x07,0x30,0x03,0x30,0x03,0x30,0x03,0x38,0x07,0x1C,0x0E,0x0C,0x0C,0x00,0x00},	// 0x43
{0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x30,0x03,0x30,0x03,0x30,0x03,0x30,0x03,0x38,0x07,0x1C,0x0E,0x0F,0xFC,0x03,0xF0,0x00,0x00},	// 0x44
{0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x30,0xC3,0x30,0xC3,0x30,0xC3,0x30,0xC3,0x30,0xC3,0x30,0xC3,0x30,0x03,0x30,0x03,0x00,0x00},	// 0x45
{0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x00,0xC3,0x00,0xC3,0x00,0xC3,0x00,0xC3,0x00,0xC3,0x00,0xC3,0x00,0x03,0x00,0x03,0x00,0x00},	// 0x46
{0x00,0x00,0x03,0xF0,0x0F,0xFC,0x1C,0x0E,0x38,0x07,0x30,0x03,0x30,0xC3,0x30,0xC3,0x30,0xC3,0x3F,0xC7,0x3F,0xC6,0x00,0x00},	// 0x47
{0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x00,0xC0,0x00,0xC0,0x00,0xC0,0x00,0xC0,0x00,0xC0,0x00,0xC0,0x3F,0xFF,0x3F,0xFF,0x00,0x00},	// 0x48
{0x00,0x00,0x00,0x00,0x00,0x00,0x30,0x03,0x30,0x03,0x3F,0xFF,0x3F,0xFF,0x30,0x03,0x30,0x03,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x49
{0x00,0x00,0x0E,0x00,0x1E,0x00,0x38,0x00,0x30,0x00,0x30,0x00,0x30,0x00,0x30,0x00,0x38,0x00,0x1F,0xFF,0x07,0xFF,0x00,0x00},	// 0x4A
{0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x00,0xC0,0x01,0xE0,0x03,0xF0,0x07,0x38,0x0E,0x1C,0x1C,0x0E,0x38,0x07,0x30,0x03,0x00,0x00},	// 0x4B
{0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x30,0x00,0x30,0x00,0x30,0x00,0x30,0x00,0x30,0x00,0x30,0x00,0x30,0x00,0x30,0x00,0x00,0x00},	// 0x4C
{0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x00,0x1E,0x00,0x78,0x01,0xE0,0x01,0xE0,0x00,0x78,0x00,0x1E,0x3F,0xFF,0x3F,0xFF,0x00,0x00},	// 0x4D
{0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x00,0x0E,0x00,0x38,0x00,0xF0,0x03,0xC0,0x07,0x00,0x1C,0x00,0x3F,0xFF,0x3F,0xFF,0x00,0x00},	// 0x4E
{0x00,0x00,0x03,0xF0,0x0F,0xFC,0x1C,0x0E,0x38,0x07,0x30,0x03,0x30,0x03,0x38,0x07,0x1C,0x0E,0x0F,0xFC,0x03,0xF0,0x00,0x00},	// 0x4F
{0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x01,0x83,0x01,0x83,0x01,0x83,0x01,0x83,0x01,0x83,0x01,0xC7,0x00,0xFE,0x00,0x7C,0x00,0x00},	// 0x50
{0x00,0x00,0x03,0xF0,0x0F,0xFC,0x1C,0x0E,0x38,0x07,0x30,0x03,0x36,0x03,0x3E,0x07,0x1C,0x0E,0x3F,0xFC,0x33,0xF0,0x00,0x00},	// 0x51
{0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x01,0x83,0x01,0x83,0x03,0x83,0x07,0x83,0x0F,0x83,0x1D,0xC7,0x38,0xFE,0x30,0x7C,0x00,0x00},	// 0x52
{0x00,0x00,0x0C,0x3C,0x1C,0x7E,0x38,0xE7,0x30,0xC3,0x30,0xC3,0x30,0xC3,0x30,0xC3,0x39,0xC7,0x1F,0x8E,0x0F,0x0C,0x00,0x00},	// 0x53
{0x00,0x00,0x00,0x00,0x00,0x03,0x00,0x03,0x00,0x03,0x3F,0xFF,0x3F,0xFF,0x00,0x03,0x00,0x03,0x00,0x03,0x00,0x00,0x00,0x00},	// 0x54
{0x00,0x00,0x07,0xFF,0x1F,0xFF,0x38,0x00,0x30,0x00,0x30,0x00,0x30,0x00,0x30,0x00,0x38,0x00,0x1F,0xFF,0x07,0xFF,0x00,0x00},	// 0x55
{0x00,0x00,0x00,0x07,0x00,0x3F,0x01,0xF8,0x0F,0xC0,0x3E,0x00,0x3E,0x00,0x0F,0xC0,0x01,0xF8,0x00,0x3F,0x00,0x07,0x00,0x00},	// 0x56
{0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x1C,0x00,0x06,0x00,0x03,0x80,0x03,0x80,0x06,0x00,0x1C,0x00,0x3F,0xFF,0x3F,0xFF,0x00,0x00},	// 0x57
{0x00,0x00,0x30,0x03,0x3C,0x0F,0x0E,0x1C,0x03,0x30,0x01,0xE0,0x01,0xE0,0x03,0x30,0x0E,0x1C,0x3C,0x0F,0x30,0x03,0x00,0x00},	// 0x58
{0x00,0x00,0x00,0x03,0x00,0x0F,0x00,0x3C,0x00,0xF0,0x3F,0xC0,0x3F,0xC0,0x00,0xF0,0x00,0x3C,0x00,0x0F,0x00,0x03,0x00,0x00},	// 0x59
{0x00,0x00,0x30,0x03,0x3C,0x03,0x3E,0x03,0x33,0x03,0x31,0xC3,0x30,0xE3,0x30,0x33,0x30,0x1F,0x30,0x0F,0x30,0x03,0x00,0x00},	// 0x5A
{0x00,0x00,0x00,0x00,0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x30,0x03,0x30,0x03,0x30,0x03,0x30,0x03,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x5B
{0x00,0x00,0x00,0x0E,0x00,0x1C,0x00,0x38,0x00,0x70,0x00,0xE0,0x01,0xC0,0x03,0x80,0x07,0x00,0x0E,0x00,0x1C,0x00,0x18,0x00},	// 0x5C
{0x00,0x00,0x00,0x00,0x00,0x00,0x30,0x03,0x30,0x03,0x30,0x03,0x30,0x03,0x3F,0xFF,0x3F,0xFF,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x5D
{0x00,0x00,0x00,0x60,0x00,0x70,0x00,0x38,0x00,0x1C,0x00,0x0E,0x00,0x07,0x00,0x0E,0x00,0x1C,0x00,0x38,0x00,0x70,0x00,0x60},	// 0x5E
{0x00,0x00,0xC0,0x00,0xC0,0x00,0xC0,0x00,0xC0,0x00,0xC0,0x00,0xC0,0x00,0xC0,0x00,0xC0,0x00,0xC0,0x00,0xC0,0x00,0xC0,0x00},	// 0x5F
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x3E,0x00,0x7E,0x00,0x4E,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x60
{0x00,0x00,0x1C,0x00,0x3E,0x40,0x33,0x60,0x33,0x60,0x33,0x60,0x33,0x60,0x33,0x60,0x33,0x60,0x3F,0xE0,0x3F,0xC0,0x00,0x00},	// 0x61
{0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x30,0xC0,0x30,0x60,0x30,0x60,0x30,0x60,0x30,0x60,0x38,0xE0,0x1F,0xC0,0x0F,0x80,0x00,0x00},	// 0x62
{0x00,0x00,0x0F,0x80,0x1F,0xC0,0x38,0xE0,0x30,0x60,0x30,0x60,0x30,0x60,0x30,0x60,0x30,0x60,0x18,0xC0,0x08,0x80,0x00,0x00},	// 0x63
{0x00,0x00,0x0F,0x80,0x1F,0xC0,0x38,0xE0,0x30,0x60,0x30,0x60,0x30,0x60,0x30,0xE0,0x30,0xC0,0x3F,0xFF,0x3F,0xFF,0x00,0x00},	// 0x64
{0x00,0x00,0x0F,0x80,0x1F,0xC0,0x3B,0xE0,0x33,0x60,0x33,0x60,0x33,0x60,0x33,0x60,0x33,0x60,0x13,0xC0,0x01,0x80,0x00,0x00},	// 0x65
{0x00,0x00,0x00,0xC0,0x00,0xC0,0x3F,0xFC,0x3F,0xFE,0x00,0xC7,0x00,0xC3,0x00,0xC3,0x00,0x03,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x66
{0x00,0x00,0x03,0x80,0xC7,0xC0,0xCE,0xE0,0xCC,0x60,0xCC,0x60,0xCC,0x60,0xCC,0x60,0xE6,0x60,0x7F,0xE0,0x3F,0xE0,0x00,0x00},	// 0x67
{0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x00,0xC0,0x00,0x60,0x00,0x60,0x00,0x60,0x00,0xE0,0x3F,0xC0,0x3F,0x80,0x00,0x00,0x00,0x00},	// 0x68
{0x00,0x00,0x00,0x00,0x00,0x00,0x30,0x00,0x30,0x60,0x3F,0xEC,0x3F,0xEC,0x30,0x00,0x30,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x69
{0x00,0x00,0x00,0x00,0x00,0x00,0x60,0x00,0xE0,0x00,0xC0,0x00,0xC0,0x60,0xFF,0xEC,0x7F,0xEC,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x6A
{0x00,0x00,0x00,0x00,0x3F,0xFF,0x3F,0xFF,0x03,0x00,0x07,0x80,0x0F,0xC0,0x1C,0xE0,0x38,0x60,0x30,0x00,0x00,0x00,0x00,0x00},	// 0x6B
{0x00,0x00,0x00,0x00,0x00,0x00,0x30,0x00,0x30,0x03,0x3F,0xFF,0x3F,0xFF,0x30,0x00,0x30,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x6C
{0x00,0x00,0x3F,0xE0,0x3F,0xC0,0x00,0xE0,0x00,0xE0,0x3F,0xC0,0x3F,0xC0,0x00,0xE0,0x00,0xE0,0x3F,0xC0,0x3F,0x80,0x00,0x00},	// 0x6D
{0x00,0x00,0x00,0x00,0x3F,0xE0,0x3F,0xE0,0x00,0x60,0x00,0x60,0x00,0x60,0x00,0x60,0x00,0xE0,0x3F,0xC0,0x3F,0x80,0x00,0x00},	// 0x6E
{0x00,0x00,0x0F,0x80,0x1F,0xC0,0x38,0xE0,0x30,0x60,0x30,0x60,0x30,0x60,0x30,0x60,0x38,0xE0,0x1F,0xC0,0x0F,0x80,0x00,0x00},	// 0x6F
{0x00,0x00,0xFF,0xE0,0xFF,0xE0,0x0C,0x60,0x18,0x60,0x18,0x60,0x18,0x60,0x18,0x60,0x1C,0xE0,0x0F,0xC0,0x07,0x80,0x00,0x00},	// 0x70
{0x00,0x00,0x07,0x80,0x0F,0xC0,0x1C,0xE0,0x18,0x60,0x18,0x60,0x18,0x60,0x18,0x60,0x0C,0x60,0xFF,0xE0,0xFF,0xE0,0x00,0x00},	// 0x71
{0x00,0x00,0x00,0x00,0x3F,0xE0,0x3F,0xE0,0x00,0xC0,0x00,0x60,0x00,0x60,0x00,0x60,0x00,0x60,0x00,0xE0,0x00,0xC0,0x00,0x00},	// 0x72
{0x00,0x00,0x11,0xC0,0x33,0xE0,0x33,0x60,0x33,0x60,0x33,0x60,0x33,0x60,0x3F,0x60,0x1E,0x40,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x73
{0x00,0x00,0x00,0x60,0x00,0x60,0x1F,0xFE,0x3F,0xFE,0x30,0x60,0x30,0x60,0x30,0x60,0x30,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x74
{0x00,0x00,0x0F,0xE0,0x1F,0xE0,0x38,0x00,0x30,0x00,0x30,0x00,0x30,0x00,0x30,0x00,0x18,0x00,0x3F,0xE0,0x3F,0xE0,0x00,0x00},	// 0x75
{0x00,0x00,0x00,0x60,0x01,0xE0,0x07,0x80,0x1E,0x00,0x38,0x00,0x38,0x00,0x1E,0x00,0x07,0x80,0x01,0xE0,0x00,0x60,0x00,0x00},	// 0x76
{0x00,0x00,0x07,0xE0,0x1F,0xE0,0x38,0x00,0x1C,0x00,0x0F,0xE0,0x0F,0xE0,0x1C,0x00,0x38,0x00,0x1F,0xE0,0x07,0xE0,0x00,0x00},	// 0x77
{0x00,0x00,0x30,0x60,0x38,0xE0,0x1D,0xC0,0x0F,0x80,0x07,0x00,0x0F,0x80,0x1D,0xC0,0x38,0xE0,0x30,0x60,0x00,0x00,0x00,0x00},	// 0x78
{0x00,0x00,0x00,0x00,0x00,0x60,0x81,0xE0,0xE7,0x80,0x7E,0x00,0x1E,0x00,0x07,0x80,0x01,0xE0,0x00,0x60,0x00,0x00,0x00,0x00},	// 0x79
{0x00,0x00,0x30,0x60,0x38,0x60,0x3C,0x60,0x36,0x60,0x33,0x60,0x31,0xE0,0x30,0xE0,0x30,0x60,0x30,0x20,0x00,0x00,0x00,0x00},	// 0x7A
{0x00,0x00,0x00,0x00,0x00,0x80,0x01,0xC0,0x1F,0xFC,0x3F,0x7E,0x70,0x07,0x60,0x03,0x60,0x03,0x60,0x03,0x00,0x00,0x00,0x00},	// 0x7B
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x3F,0xBF,0x3F,0xBF,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x7C
{0x00,0x00,0x00,0x00,0x60,0x03,0x60,0x03,0x60,0x03,0x70,0x07,0x3F,0x7E,0x1F,0xFC,0x01,0xC0,0x00,0x80,0x00,0x00,0x00,0x00},	// 0x7D
{0x00,0x00,0x00,0x10,0x00,0x18,0x00,0x0C,0x00,0x04,0x00,0x0C,0x00,0x18,0x00,0x10,0x00,0x18,0x00,0x0C,0x00,0x04,0x00,0x00},	// 0x7E
{0x00,0x00,0x0F,0x00,0x0F,0x80,0x0C,0xC0,0x0C,0x60,0x0C,0x30,0x0C,0x30,0x0C,0x60,0x0C,0xC0,0x0F,0x80,0x0F,0x00,0x00,0x00},	// 0x7F
{0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x78,0x00,0xFC,0x00,0xCC,0x00,0xCC,0x00,0xFC,0x00,0x78,0x00,0x00,0x00,0x00,0x00,0x00},	// 0x80 °-sign
};

//Lcd help data
//Display buffer
char *oldbuf = " ";
int bcolor = DARK_BLUE; //Standard Background Color

//METER
int sv_old = 0;
int smax = 0;

////////////////
//Declarations//
////////////////

//MISC
int main(void);

//ILI9341 LCD Basic Functions
void lcd_send(int, int); //Write a byte of data via PARALLEL
void lcd_set_xy(int, int);
void lcd_cls(int);
void lcd_draw_pixel(int);
void lcd_putchar(int, int, int, int, int, int);
void lcd_putstring(int, int, char*, int, int, int);

//Extended LCD functions
void show_frequency(long, int, int);
void show_mem_number(int);
void show_sideband(int, int);
void show_voltage(int);
void show_temp(int);
void show_vfo(int, int);
void show_split(int, int);
void show_scan_status(int, int);
void show_tone(int, int);
void show_agc(int, int);
void draw_meter_scale(int, int);
void reset_smax(void);
void smeter(int, int);
void show_msg(char*, int);

//STRING FUNCTIONS
int int2asc(long, int, char*, int);
int strlen(char *s);

//PARALLEL write data or command to LCD
void lcd_send(int dc, int val)
{
if(!dc) //Cmd (0) or Data(1)?
{
   LCDCTRLPORT &= ~(LCDRS); //Cmd=0
}
else
{
   LCDCTRLPORT |= LCDRS; //Data=1
}
LCDCTRLPORT |= LCDRD;

LCDDATAPORT = val;
LCDCTRLPORT &= ~(LCDWR); //Write operation
LCDCTRLPORT |= LCDWR;
}

//Init LCD to vertical alignement and 16-bit color mode
void lcd_init(void)
{
lcd_send(LCD_CMD, 0xCF);
lcd_send(LCD_DATA, 0x00);
lcd_send(LCD_DATA, 0xc1);
lcd_send(LCD_DATA, 0x30);

lcd_send(LCD_CMD, 0xed);
    lcd_send(LCD_DATA, 0x64);
    lcd_send(LCD_DATA, 0x03);
    lcd_send(LCD_DATA, 0x12);
    lcd_send(LCD_DATA, 0x81);

lcd_send(LCD_CMD, 0xcb);
    lcd_send(LCD_DATA, 0x39);
    lcd_send(LCD_DATA, 0x2c);
    lcd_send(LCD_DATA, 0x00);
    lcd_send(LCD_DATA, 0x34);
    lcd_send(LCD_DATA, 0x02);

    lcd_send(LCD_CMD, 0xea);
lcd_send(LCD_DATA, 0x00);
lcd_send(LCD_DATA, 0x00);

    lcd_send(LCD_CMD, 0xe8);
lcd_send(LCD_DATA, 0x85);
lcd_send(LCD_DATA, 0x10);
lcd_send(LCD_DATA, 0x79);

    lcd_send(LCD_CMD, 0xC0); // Power control
    lcd_send(LCD_DATA, 0x23); // VRH[5:0]

    lcd_send(LCD_CMD, 0xC1); // Power control
    lcd_send(LCD_DATA, 0x10); // SAP[2:0];BT[3:0]

    lcd_send(LCD_CMD, 0xC5); // VCM control
    lcd_send(LCD_DATA, 0x3e);
    lcd_send(LCD_DATA, 0x28);

    lcd_send(LCD_CMD, 0xC7); // VCM control2
    lcd_send(LCD_DATA, 0x86);

    lcd_send(LCD_CMD, 0x36); // Memory Access Control
    lcd_send(LCD_DATA, 0x88); // C8

    lcd_send(LCD_CMD, 0x3A);
    lcd_send(LCD_DATA, 0x55);

    lcd_send(LCD_CMD, 0xB1);
    lcd_send(LCD_DATA, 0x00);
    lcd_send(LCD_DATA, 0x18);

    lcd_send(LCD_CMD, 0xB6); // Display Function Control
    lcd_send(LCD_DATA, 0x08);
    lcd_send(LCD_DATA, 0x82);
    lcd_send(LCD_DATA, 0x27);

    lcd_send(LCD_CMD, 0xF2); // 3Gamma Function Disable
    lcd_send(LCD_DATA, 0x00);

    lcd_send(LCD_CMD, 0x26); // Gamma curve selected
    lcd_send(LCD_DATA, 0x01);

    lcd_send(LCD_CMD, 0xE0); // Set Gamma
    lcd_send(LCD_DATA, 0x0F);
    lcd_send(LCD_DATA, 0x31);
    lcd_send(LCD_DATA, 0x2B);
    lcd_send(LCD_DATA, 0x0C);
    lcd_send(LCD_DATA, 0x0E);
    lcd_send(LCD_DATA, 0x08);
    lcd_send(LCD_DATA, 0x4E);
    lcd_send(LCD_DATA, 0xF1);
    lcd_send(LCD_DATA, 0x37);
    lcd_send(LCD_DATA, 0x07);
    lcd_send(LCD_DATA, 0x10);
    lcd_send(LCD_DATA, 0x03);
    lcd_send(LCD_DATA, 0x0E);
    lcd_send(LCD_DATA, 0x09);
    lcd_send(LCD_DATA, 0x00);

    lcd_send(LCD_CMD, 0xE1); // Set Gamma
    lcd_send(LCD_DATA, 0x00);
    lcd_send(LCD_DATA, 0x0E);
    lcd_send(LCD_DATA, 0x14);
    lcd_send(LCD_DATA, 0x03);
    lcd_send(LCD_DATA, 0x11);
    lcd_send(LCD_DATA, 0x07);
    lcd_send(LCD_DATA, 0x31);
    lcd_send(LCD_DATA, 0xC1);
    lcd_send(LCD_DATA, 0x48);
    lcd_send(LCD_DATA, 0x08);
    lcd_send(LCD_DATA, 0x0F);
    lcd_send(LCD_DATA, 0x0C);
    lcd_send(LCD_DATA, 0x31);
    lcd_send(LCD_DATA, 0x36);
    lcd_send(LCD_DATA, 0x0F);

    lcd_send(LCD_CMD, 0x11); // Sleep out
    _delay_ms(120);
    lcd_send(LCD_CMD, 0x2c);

    lcd_send(LCD_CMD, 0x29); // Display on
    lcd_send(LCD_CMD, 0x2c);

}

void lcd_set_xy(int x, int y)
{
//X
lcd_send(LCD_CMD, 0x2B);
    lcd_send(LCD_DATA, x >> 8);
    lcd_send(LCD_DATA, x & 0xFF);
    lcd_send(LCD_CMD, 0x2c);

    //Y
    lcd_send(LCD_CMD, 0x2A);
    lcd_send(LCD_DATA, y >> 8);
    lcd_send(LCD_DATA, y & 0xFF);
    lcd_send(LCD_CMD, 0x2c);
}

void lcd_draw_pixel(int color)
{
    lcd_send(LCD_DATA, color >> 8);
    lcd_send(LCD_DATA, color & 0xFF);
}

void lcd_cls(int bcolor)
{
int x;
unsigned char y;

lcd_set_xy(0, 0);
for(x = 0; x < LCD_WIDTH; x++)
{
        for(y = 0; y < LCD_HEIGHT; y++)
        {
lcd_draw_pixel(bcolor);
}
}
}

//Write character from font set to destination on screen
void lcd_putchar(int x, int y, int c, int size, int fcolor, int bcolor)
{
    int x0;
    int t0, t1, t2, t3, u;

    x0 = x;
    for(t0 = 0; t0 < FONTWIDTH * 2; t0 += 2)
    {
for(t1 = 0; t1 < size; t1++)
{
   u = xchar[c][t0 + 1] + (xchar[c][t0] << 8);
   lcd_set_xy(x0, y);
   for(t2 = 16; t2 >= 0; t2--)
   {
   if(u & (1 << t2))
   {
   for(t3 = 0; t3 < size; t3++)
   {
        lcd_draw_pixel(fcolor);
        }
       }
       else
       {
        for(t3 = 0; t3 < size; t3++)
   {
        lcd_draw_pixel(bcolor);
        }
       }
   }
   x0++;
}
}
}

//Print String to LCD
void lcd_putstring(int x, int y, char *text, int size, int fc, int bc)
{
int t1 = 0, x0;

x0 = x;
while(text[t1])
{
lcd_putchar(x0, y, text[t1], size, fc, bc);
x0 += (size * FONTWIDTH);
t1++;
}
}

//Convert a number to a string and print it
//col, row: Coordinates, Num: int or long to be displayed
//dec: Set position of decimal separator
//
//inv: Set to 1 if inverted charactor is required
void lcd_putnumber(int x, int y, long num, int dec, int lsize, int fc, int bc)
{
    char *s = malloc(16);
if(s != NULL)
{
   int2asc(num, dec, s, 16);
   lcd_putstring(x, y, s, lsize, fc, bc);
   free(s);
}
else
{
lcd_putstring(x, y, "Error", lsize, fc, bc);
}
}

   ///////////////////////////////////////
  // Data Display Functions for Radio //
 ///////////////////////////////////////
//Current frequency (double letter height)
void show_frequency(long f, int refresh, int bcolor)
{
char *buf;
int t1 = 0;
int x0 = 90, y0 = 110;
int size = 2;

if(f < 10000000)
{
x0 = 9;
}

if(f == -1)
{
lcd_putstring(x0, y0, " ", 3, YELLOW, bcolor);
return;
}

if(f == 0)
{
lcd_putstring(x0, y0, " -------", 3, YELLOW, bcolor);
return;
}

buf = malloc(10);

//Init buffer string
for(t1 = 0; t1 < 10; t1++)
{
   *(buf + t1) = 0;
}

if(f)
{
   int2asc(f / 100, 1, buf, 9);
}
else
{
for(t1 = 0; t1 < 8; t1++)
{
buf[t1] = 32;
}
}

//Display buffer (but only the letters that have changed)
for(t1 = 0; *(buf + t1); t1++)
{
if((*(oldbuf + t1) != *(buf + t1)) || refresh)
{
   lcd_putchar(x0 + t1 * FONTWIDTH * size, y0, *(buf + t1), size, YELLOW, bcolor);
}
}

//Copy current buffer to storing variable
t1 = 0;
while(*(buf + t1))
{
*(oldbuf + t1) = *(buf + t1);
t1++;
}

free(buf);
}

//VFO
void show_vfo(int nvfo, int bcolor)
{
int xpos = 5, ypos = ROW1;

lcd_putstring(xpos, ypos, "VFO", 1, GRAY, bcolor);
lcd_putchar(xpos + 3 * FONTWIDTH, ypos, nvfo + 65, 1, GRAY, bcolor);

}

//Show memory place by number
void show_mem_number(int mem_addr)
{
int xpos = 70, ypos = ROW1;

if(mem_addr == -1)
{
lcd_putstring(xpos + FONTWIDTH * 2, ypos, "--", 1, LIGHT_GRAY, bcolor);
return;
}

//Show number of mem place
lcd_putstring(xpos, ypos, "M", 1, WHITE, bcolor);

if(mem_addr < 10)
{
    lcd_putnumber(xpos + 1 * FONTWIDTH, ypos, 0, -1, 1, LIGHT_GRAY, bcolor);
    lcd_putnumber(xpos + 2 * FONTWIDTH, ypos, mem_addr, -1, 1,LIGHT_GRAY, bcolor);
}
else
{
lcd_putnumber(xpos + 1 * FONTWIDTH, ypos, mem_addr, -1, 1, LIGHT_GRAY, bcolor);
}
}

void show_split(int sp_status, int bcolor)
{
int xpos = 120, ypos = ROW1;
char *splitstr = "SPLIT";

//Write string to position
if(!sp_status)
{
   lcd_putstring(xpos, ypos, splitstr, 1, WHITE, bcolor);
}
else
{
   lcd_putstring(xpos, ypos, splitstr, 1, bcolor, WHITE);
}
}

//Scan operation
void show_scan_status(int status, int bc)
{
int xpos = 190, ypos = ROW1;

switch(status)
{
case 0: lcd_putstring(xpos, ypos, "SCAN", 1, WHITE, bcolor);
       break;
case 1: lcd_putstring(xpos, ypos, "VFO ", 1, WHITE, bcolor);
       break;
case 2: lcd_putstring(xpos, ypos, "VFO*", 1, WHITE, bcolor);
       break;
case 3: lcd_putstring(xpos, ypos, "BND ", 1, WHITE, bcolor);
       break;
case 4: lcd_putstring(xpos, ypos, "BND*", 1, WHITE, bcolor);
       break;
}
}

//Current sideband display
void show_sideband(int sb, int bc)
{
int xpos = 250, ypos = ROW1;
char *sidebandstr[] = {"LSB", "USB"};

//Write string to position
lcd_putstring(xpos, ypos, sidebandstr[sb], 1, YELLOW, bc);
}

//Battery voltage display
void show_voltage(int bc)
{
    char *buf;
int t1;
int xpos = 250, ypos = ROW2;
int fc = LIGHT_BLUE;

int adc_v;
    double v1;

//Measure current voltage
//v1 = (double) get_adc(3) * 5 / 1024 * 3 * 10; !!!!
v1 = 121;
    adc_v = (int) v1;

   if(v1 < 110)
   {
fc = RED;
}

if(v1 > 150)
   {
fc = LIGHT_RED;
}

lcd_putstring(xpos, ypos, " ", 1, 0, bc);
buf = malloc(10);

//Init buffer string
for(t1 = 0; t1 < 10; t1++)
{
   *(buf + t1) = 0;
}

    //Display value
    int2asc(adc_v, 1, buf, 6);
    lcd_putstring(xpos, ypos, buf, 1, fc, bc);
lcd_putchar(xpos + strlen(buf) * FONTWIDTH, ypos, 'V', 1, fc, bc);

//Free mem
free(buf);
}

//Temperature display
void show_temp(int bc)
{
    char *buf;
int t1, fc;
int xpos = 250, ypos = ROW3;

int adc_t;
    double temp1;

//Measure current voltage
//temp1 = (double) get_adc(2) * 5 / 1024 * 3 * 10; !!!!
temp1 = 343;
    adc_t = (int) temp1;

lcd_putstring(xpos, ypos, " ", 1, WHITE, bc);
buf = malloc(10);

//Init buffer string
for(t1 = 0; t1 < 10; t1++)
{
   *(buf + t1) = 0;
}

    if(adc_t < 300)
    {
fc = LIGHT_BLUE;
}
if(adc_t >= 300 && adc_t < 600)
    {
fc = LIGHT_GREEN;
}
if(adc_t >= 600)
    {
fc = LIGHT_RED;
}
    //Display value
    int2asc(adc_t, 1, buf, 6);
    lcd_putstring(xpos, ypos, buf, 1, fc, bc);
lcd_putchar(xpos + strlen(buf) * FONTWIDTH, ypos, 0x80, 1, fc, bc);

//Free mem
free(buf);
}

//Tone pitch
void show_tone(int tone, int bc)
{
int xpos = 5, ypos = ROW2;
char *tstr[] = {"HIGH", "MID ", "LOW ", "XLOW"};
lcd_putstring(xpos, ypos, tstr[tone], 1, WHITE, bc);
}

//AGC speed
void show_agc(int agc, int bc)
{
int xpos = 70, ypos = ROW2;
char *agcstr[] = {"FAST ", "NORM ", "SLOW ", "XSLOW"};
lcd_putstring(xpos, ypos, agcstr[agc], 1, WHITE, bc);
}

//Draw TX or RX meter scale
void draw_meter_scale(int scaletype, int bc)
{
int x = 5, y = ROW10;

if(!scaletype)
{
lcd_putstring(x, y, "S1 3 5 7 9 +10 +20dB", 1, WHITE, bcolor);
}
else
{
lcd_putstring(x, y, "P 1 2 4 6 8 10 20W", 1, WHITE, bcolor);
}
}

//S-Meter bargraph
void smeter(int value, int bc)
{
int v, t1, t2;
int maxs = 200; //Max.value to be displayed in pixels
int x = 5, y = ROW9 + 5; //Position omn screen
static int smaxold;

//Clear meter
if(value == -1) //Fullclear
{
for(t1 = 0; t1 < maxs; t1 += 4)
   {
   lcd_set_xy(x + t1, y);
   for(t2 = 0; t2 < 4; t2++)
   {
   lcd_draw_pixel(bc);
   }
}
return;
}

v = value;
if(v > maxs)
{
v = maxs;
}

if(v < smaxold)
{
for(t1 = v; t1 < smaxold; t1 += 4)
   {
   lcd_set_xy(x + t1, y);
   for(t2 = 0; t2 < 4; t2++)
   {
   lcd_draw_pixel(bc);
   }
}
smaxold = v;
return;
}

//Draw bar
for(t1 = smaxold; t1 < v; t1 += 4)
{
lcd_set_xy(x + t1, y);
for(t2 = 0; t2 < 4; t2++)
{
lcd_draw_pixel(WHITE);
}
}

if(smaxold < v)
{
smaxold = v;
}

}

//Reset max value of s meter
void reset_smax(void)
{
//int s = get_s_value(); !!!!
int s = 50;

smax = 0;
sv_old = 0;
smeter(s, bcolor);
}

void show_msg(char *msg, int bc)
{
int x = 5, y = ROW11, t1;

if(!strlen(msg))
{
for(t1 = 0; t1 < 26; t1++)
{
lcd_putchar(t1 * FONTWIDTH, y, 32, 1, bc, bc);
}
return;
}

lcd_putstring(x, y, msg, 1, LIGHT_GRAY, bc);
}

//////////////////////
 // STRING FUNCTIONS //
//////////////////////
//INT 2 ASC
int int2asc(long num, int dec, char *buf, int buflen)
{
    int i, c, xp = 0, neg = 0;
    long n, dd = 1E09;

    if(!num)
{
   *buf++ = '0';
*buf = 0;
return 1;
}

    if(num < 0)
    {
     neg = 1;
   n = num * -1;
    }
    else
    {
   n = num;
    }

    //Fill buffer with \0
    for(i = 0; i < 12; i++)
    {
   *(buf + i) = 0;
    }

    c = 9; //Max. number of displayable digits
    while(dd)
    {
   i = n / dd;
   n = n - i * dd;

   *(buf + 9 - c + xp) = i + 48;
   dd /= 10;
   if(c == dec && dec)
   {
       *(buf + 9 - c + ++xp) = '.';
   }
   c--;
    }

    //Search for 1st char different from '0'
    i = 0;
    while(*(buf + i) == 48)
    {
   *(buf + i++) = 32;
    }

    //Add minus-sign if neccessary
    if(neg)
    {
   *(buf + --i) = '-';
    }

    //Eleminate leading spaces
    c = 0;
    while(*(buf + i))
    {
   *(buf + c++) = *(buf + i++);
    }
    *(buf + c) = 0;

return c;
}

//STRLEN
int strlen(char *s)
{
   int t1 = 0;

   while(*(s + t1++));

   return (t1 - 1);
}

int main(void)
{
long t1;
    LCDDATADDR = 0xFF;
    LCDCTRLDDR = 0x0F;

    LCDCTRLPORT &= ~(LCDRES); //0
_delay_ms(5);
    LCDCTRLPORT |= LCDRES; //1
    _delay_ms(5);

    lcd_init();
    lcd_cls(DARK_BLUE);
    for(t1 = 14235100; t1 < 14235500; t1 += 100)
    {
        show_frequency(t1, 0, bcolor);
    }
    show_mem_number(11);
    show_sideband(0, bcolor);
    show_vfo(0, bcolor);
    show_voltage(bcolor);
    show_temp(bcolor);
    show_split(0, bcolor);
    show_agc(2, bcolor);
    show_tone(2, bcolor);
    show_scan_status(0, bcolor);
    draw_meter_scale(0, bcolor);

    lcd_putstring(270, 114, "KHz", 1, YELLOW, bcolor);
    show_msg("DK7IH 2019", bcolor);

    while(1)
    {
for(t1 = 0; t1 < 200; t1++)
{
smeter(t1, bcolor);
}
for(t1 = 200; t1 > 0; t1--)
{
smeter(t1, bcolor);
}
smeter(-1, bcolor);
}

return 0;
}